/*
  This implementation specific to Arduino Mini-Pro 328 running at 3.3V
  and used with a NOKIA 5110 Craphic LCD.

  Built under Arduino 1.0.5
*/

#include <EEPROM.h>
#include <Streaming.h>
#include "Defines.h" // Nokia 5110 LCD pin usage as controlled by "ScrnFuncts.ino"

// constants
const int BAUD = 9600; // any standard serial value: 300 - 115200
const int EEaddr = 0; // EEPROM address for storing WPM
const int EEaddr1 = 2; // EEPROM address for LCD address
// Arduino 328P pins (not physical)

const byte ContrastPin = 8; // D8 low activates the Contrast adjustment

// global prog variables

byte nRow; // line count (0-5 for NOKIA LCD)
byte nColumn; // character count (0-11 for NOKIA LCD)
byte NOKIAcontrast; // LCD initialization contrast values B0 thru BF

char temp;

// Character array pointers
char* PROGMEM msg0[] = {"TerminalTest(C)2014 by M. Burnette Ver 0.000000"}; // 72 characters == full screen
char* PROGMEM msg1[] = {"The quick Brown Fox Jumps over The Lazy DogBack Press ENTER "};
char* PROGMEM BlankLine[] = {" "}; // Nokia 12 x 6 (84 * 48)

void setup(void)
  {

    pinMode(ContrastPin, INPUT);
    digitalWrite(ContrastPin, HIGH); // activate internal pullup resistor

    Serial.begin(BAUD);
    Serial << (F("(c) 2013 - 2014 by M. R. Burnette")) << endl;
    Serial << (F("Free RAM available: ")) ;
    Serial << freeRam() << endl;
    Serial << (F("Version 0.20140126")) << endl;
    ReStart: // Come back here if LCD contract is changed
    // Read the EEPROM to determine if display is using a custom contrast value
    NOKIAcontrast = EEPROM.read(EEaddr1);
    // Set the Nokia LCD Contrast to default or reset if EEPROM is corrupt or set to new value
    if (NOKIAcontrast < 0xB0 || NOKIAcontrast > 0xBF) NOKIAcontrast = 0xB2;
    // LCD
    LcdInitialise();
    LcdClear();
    LcdString(*msg0);
    delay(2000);
    if (!digitalRead(ContrastPin)) {
        NOKIAcontrast++;
        if (NOKIAcontrast > 0xBF) NOKIAcontrast = 0xB0;
        EEPROM.write(EEaddr1, NOKIAcontrast);
        goto ReStart;
    }
    // Set WPM default and write to EEPROM IF Morse Key is closed at this point...

    LcdClear(); delay(500); nRow = 1;
    LcdString(*msg1);
    nRow = 0; nColumn = 0;
    gotoXY(nColumn, nRow);
    do {} while (Serial.available() == 0) ;
    LcdClear(); // nRow = 0; nColumn = 0 done by function LcdClear()
}

void loop(void)
{
    if (Serial.available() > 0)
    {
      char temp = Serial.read();
      Serial << temp; // for diagnostic and Arduino term echo
      switch (temp)
        {
        case '\n' :
        ++nRow; nColumn = 0;
        if (nRow == 6) nRow = 0;
        LcdString(BlankLine[0]); // clear line

        case '\r' :
        ++nRow; nColumn = 0;
        if (nRow == 6) nRow = 0;
        LcdString(BlankLine[0]); // clear line

        default :
        gotoXY(nColumn, nRow);
        if (temp > 31 && temp < 128) SendCharLCD(temp);
        if (nColumn == 0 ) LcdString(BlankLine[0]); // clear new line
        }
    }
}